## Slide 1: Rodent Automated Training
Verification and Validation
Ellie Degen, Sara McCutcheon, Zoe Orenstein
Client: Dr. Keith Hengen
March 6, 2019

## Slide 2: Changes to Design Specifications
https://www.pdn.cam.ac.uk/images/homepage/Carousel/best-15-wpid-free-mice-silhouette-vector-image.jpg/image_view_fullscreen
https://www.amazon.com/Vinyl-Stickers-Rat-Silhouette-Sticker/dp/B0115GNWZW
RAT
MOUSE
Notes: Decreasing cage dimensions

## Slide 3: Changes to Design Specifications
6x6x9” living space
3x6x9” antechamber
Transparent wall between cages
Notes: Decreasing cage dimensions

## Slide 4: Changes to Design Specifications
9 PM - 9 AM
WATER DEPRIVATION
TRAINING
9 AM - 10 AM
10 AM - 9 PM (the next day)
35 HRS UNRESTRICTED WATER
Notes: New water deprivation method and testing schedule
No water access for 12 hours prior to training
Recovery day after training
Rodent will no longer initiate training → removal of beam break
9am training start time
Because of this fixed testing schedule,
Rodent will no longer initiate training
no longer a need for beam break system

## Slide 5: Changes to Design Specifications
Wall Opening
Screen
Speaker
Water System
Goal-Post Head Fixation
Old
New
Notes: Nose poke hole removed
Holes for water spouts
Head fixation 1.5 inches away from water spouts
Speaker closer to water spouts
Antechamber no longer sound proof

## Slide 6: Verification Plan
Screens
Capacitive Touch
Sensor
Solenoid Valve
Lights
Speaker
Cage design
Notes: UPDATED

## Slide 7
Screen Verification
Two screens
Display images at a programmed time
Switch images after five minutes
Notes: two screens connected to arduinos
Two goals
  to verify if the screens display the correct images
  To verify if we can display the images on a time schedule

## Slide 8: Touch Sensor Verification
Measure baseline capacitance
Set a “lick” threshold
Disrupt the spout capacitance with a finger tap
Observe valve opening
Notes: measure baseline

## Slide 9: Valve Verification - Valve Opening
Provide 5V to a driving motor
Solenoid Valve Opens
Observe water pass through valve
Notes: UPDATED

## Slide 10: Valve Verification - Correct Amount of Water
50 repeats: open valve for 0.5 sec, close for 1 sec
Measure total volume of water dispensed
0.5-0.6 mL delivered total?
If yes, repeat test five times
If no, increase/decrease the open time by 0.1 sec
Notes: to verify that the valve dispenses the correct amount of water
if yes, repeat five times for consistency

## Slide 11: Speaker Verification Lights Verification
Present a 1,000 Hz tone at 50 dB for one second
Turn on/off a string of LED lights five times at two second intervals
https://www.mightyape.co.nz/product/aurora-led-light-strip-blue/22166761
https://www.adafruit.com/product/1669
https://www.mightyape.co.nz/product/aurora-led-light-strip-blue/22166761

## Slide 12: Cage Design Verification
observe mouse for 24 hours
Side-view (two normal cages)
Top-view (two normal cages)
RAT cage will have an antechamber
COMPARE TO DIMENSIONS OF EXISTING CAGES
PLACE ON HENGEN LAB SHELVES
CONFIRM THE ANTECHAMBER IS INACCESSIBLE
Notes: compare the dimensions to existing cages
make sure the cage can fit on the Hengen lab shelves
observe a mouse in the cage for 24 hours to confirm the antechamber is anacessible

## Slide 13: Validation Testing Plan
Notes: our validation plan is constructed to make sure that all our hardware components work together
  raspberry pi
  four arduinos
  screens
  valves
  capacitve sensor
  lights and speaker
  thermistor

## Slide 14: Rodent Training Protocol
Notes: we will validate that the components work together by testing the training protocol
12 hours of water deprivation
Spouts do not deliver water when licked
At 9am (the beginning of training):
1,000 Hz tone plays for two seconds
String of LEDs lights up
Each screen lights up and displays an image

## Slide 15: Rodent Training Protocol: Setup
Goal-Post Head Fixation
Screens
Water Reservoir
Tubing
Spout
Speaker
Wall Opening
Notes: the physical setup for our training protocol
spouts are connected to capacitive sensors
each spout corresponds to the screen it is in front of
one screen and spout will be the "correct choice," and the other pair will be the incorrect choice

## Slide 16: Rodent Training Protocol
Wall Opening Screen Speaker
Water System Goal-Post Head Fixation
Screens display pair of images
Rodent licks correct spout
Lick registered by Capacitive Sensor and recorded
Solenoid Valve opens, Light and Sound indicate correct choice
Rodent receives water reward at spout
Notes: UPDATED
If the mouse licks the correct spout
Capacitive sensor registers lick
Signal sent to open solenoid valve
Water released at the spout
2,000 Hz tone played for 2 sec
LED strip lights up above screens
4. Screens remain on the images for 5 sec
5. Screens shut off for 5 sec
6. Cycle repeats with new images

## Slide 17: Rodent Training Protocol
Wall Opening Screen Speaker
Water System Goal-Post Head Fixation
Screens display pair of images
Rodent licks incorrect spout
Solenoid Valve remains closed
System pauses for 5 seconds with screens still on as “timeout” punishment
Notes: UPDATED
If the mouse licks the correct spout
Capacitive sensor registers lick
Signal sent to open solenoid valve
Water released at the spout
2,000 Hz tone played for 2 sec
LED strip lights up above screens
4. Screens remain on the images for 5 sec
5. Screens shut off for 5 sec
6. Cycle repeats with new images

## Slide 18: FDA Approval Process
This cage is designed for rodent studies and therefore does not require FDA approval.
The Hengen lab has approval from the Institutional Animal Care and Use Committee (IACUC) to use this cage with mice.

## Slide 19: Status of Product: Cage, Screens, Lights, Sound, Temperature, Humidity
Cage components have been laser cut
Walls, floor, ceiling, and antechamber
Components awaiting assembly
https://www.mightyape.co.nz/product/aurora-led-light-strip-blue/22166761
Screens controlled by Arduinos
One Arduino per screen
Light, sound, temperature/humidity
To-be assembled

## Slide 20: Status of Product: Water Delivery
Water reservoir
Spout
Solenoid Valve
Arduino Mega
Capacitive Touch Sensors
Driving Motor
Notes: Arduino-controlled solenoid valve
Capacitive touch sensor in the same circuit
Reservoir, stopper, tubing, and spout connected

## Slide 21: Proof of Concept: Water Delivery System
Testing of the solenoid valve
Arduino Mega
Solenoid Valve
Driving Motor
Notes: UPDATED
Valve and driving motor circuit connected to an Arduino
Tube placed at the valve’s bottom opening
Water poured into the top opening
Code uploaded to the Arduino
Opened the valve for 2 sec, closed for 2 sec
Valve opening → movement of water to the bottom tube

## Slide 22: Proof of Concept: Water Delivery System
Testing of the capacitive sensor
MPR121 sensor board connected to an Arduino
Code uploaded to the Arduino
Alert message printed upon touching any of the 12 sensors
Tap with finger
Notes: demonstrating that the capacitive sensor could collect input at a specific location (touch) and then execute a command (print readout).

## Slide 23: Proof of Concept: Screens
An arduino connected to each of two screens
Arduino code written to display a different image on each screen
Uploading Arduino code → screens displayed the images
https://suncatcherstudio.com/patterns/cat-silhouettes/
https://suncatcherstudio.com/patterns/cat-silhouettes/

## Slide 24: Proof of Concept: Raspberry Pi Controlling Arduino
An existing Hengen lab setup demonstrates feasibility
Raspberry Pi signals to an Arduino
Arduino turns lights on/off
Time schedule based on circadian rhythm
https://freebiesupply.com/logos/arduino-logo/
https://www.raspberrypi.org/trademark-rules/
Notes: to prove a raspberry pi can control an arduino, we looked to an existing setup in the Hengen lab
raspberry pi sets a time schedule for an arduino, which turns on and off lights based on the circadian rhythm of the rats

## Slide 25: Thank you!